## Slide 1: BRIDGE DESIGN
Chapter 3:
ANALYTICAL PROCEDURE
Dr Shahiron Shahidan
shahiron@uthm.edu.my
drshahironshahidan.weebly.com

## Slide 2: Outline
Fundamental Concepts
Influence line Analysis
Collapse Analysis
Grillage Analysis

## Slide 3: 3.1 Fundamental Concepts
Structural analysis is essential in bridge analysis. It is part of simplified mathematical modelling of the response of a structure to the applied loading.
Model are based on the idealizations of the structural behaviour of the material, depending upon the simplifying assumption in modelling.

## Slide 4
Example of idealizations introduced in the modelling process:
The physical dimension of the structural components are idealised. Eq: skeletal structures are represented by a series of line element and joint are assumed to be negligible size.
Material behaviour is simplified. Eq: The stress- strain characteristic of concrete/ steel is assumed to be linearly elastic and then perfectly plastic.
The implications of actions which are included in the analytical process itself are frequently ignored. Eq: The possible effects of change of geometry causing local instability are rarely, if ever accounted for in the analysis

## Slide 5: Stress distribution on the bridges

## Slide 6: Bridges Failure
The entire span of the Interstate 35W bridge collapsed in Minneapolis, 2007
Mianus Bridge, Greenwich, June 28, 1983
Putrajaya, Malaysia, 2013

## Slide 7: 3.2 INFLUENCE LINES

## Slide 8: 3.2.1 Introduction
In this chapter will be discussed:
  the moving load from one point to another point such as the live loads for bridge
  because of the moving vehicles
  represents the variation of the reaction, shear, moment or deflection at a specific point in a member as a concentrated force moves over the member.

## Slide 9: 3.2.2 INFLUENCE LINES FOR BEAMS
  Procedures in constructing the influence lines:
    allow a one unit load (either 1kN, 1N, 1kip or 1 ton) to move over the beam from left to right.
    find the values of shear force or bending moment at the point under consideration as the unit load moves over the beam from left to right.
    plot the values of the shear force or bending moment over the length of the beam computed for the point under consideration

## Slide 10: EX:1 (Variations of reaction)
Solution:

## Slide 13
EX:2 (Variations of reaction)
Solution: (a)

## Slide 14
Solution: (b)

## Slide 16: 3.2.3 -QUALITATIVE INFLUENCED LINES – -MULLER-BRESLAU’S PRINCIPLE-
The principle gives only a procedure to determine of the influence line of a parameter for a determinate /indeterminate structure
But using the basic understanding of the influence lines, the magnitudes of the influence lines also can be computed
In order to draw the shape of the influence lines properly, the capacity of the beam to resist the parameter investigated (reaction, bending moment, shear force, etc.), at that point, must be removed
The principle states : The influence line for a function (e.g. reaction, shear, moment) at a point, is to the same scale as the deflected shape of the beam when the beam is acted upon by that function.
  The capacity of the beam to resist that parameter, at that point, must be removed.
  Then allow the beam to deflect under that parameter
  Positive directions of the forces are the same as before

## Slide 17: 3.2.4 -QUALITATIVE INFLUENCE LINES : PROBLEMS
3.2.4.1 Influence Line for a Determinate Beam by Muller-
Breslau’s Method (Simply Supported Beam-Pin Join)
Influence line for Reaction at A
Deflection, y
Remove the ability to resist movement in the vertical direction at A by using a guided roller

## Slide 18: 3.2.4.2 Influence Lines for a Determinate Beam by Muller- Breslau’s Method (Cantilever beam-fixed support)
Influence line for Reaction at A
Use a double roller to transmit moments and axial load at the fixed support. Vertical reaction will not transmit horizontal reaction.

## Slide 19: 3.2.4.3 Influence Lines for a Determinate Beam by Muller- Breslau’s Method (Indeterminate Beam-Shear)
Influence Line for Reaction at indeterminate beam
At roller support, consider the vertical reaction at this point.

## Slide 20: 3.2.4.4 Influence Lines for a Determinate Beam by Muller- Breslau’s Method (Shear at the mid-span)
Influence Line for Shear at C
Remove the ability to resist shear at point C with roller connection. Applying a positive shear force to the beam at C and allows the deflection.

## Slide 21: 3.2.4.5 Influence Lines for a Determinate Beam by Muller- Breslau’s Method (Shear at the cantilever beam)
Influence Line for Shear at C
A roller guide must be placed at C, the positive shear is applied. The left segment of the beam does not deflect due to fixed support.

## Slide 22: 3.2.4.6 Influence Lines for a Determinate Beam by Muller- Breslau’s Method (Moment at the mid-span)
Influence Line for Bending Moment at C
Remove the ability to resist moment at C by using hinge. Moments will occur at both segments.

## Slide 23: Ex :Draw the influence lines for the vertical reaction at D and the shear at E.
10m
10m
15m
15m
If the change in shear at point E is equal to 1, find the shear value at points E and C.

## Slide 24: 3.5 INFLUENCE LINE FOR FLOOR GIRDERS Floor systems are constructed as shown in figure below,

## Slide 25: 3.5 INFLUENCE LINES FOR FLOOR GIRDERS (Cont’d)

## Slide 26: 3.5 INFLUENCE LINES FOR FLOOR GIRDERS (Cont’d)
3.5.1 Force Equilibrium Method:
Draw the Influence Lines for: (a) Shear in panel CD of the girder; and (b) the moment at E.
A
C
D
E
F
B
B´
A´
D´
C´
E´
F´
x
5 spaces @ 10´ each = 50 ft

## Slide 27
5.5.2 Place load over region A´B´ (0 < x < 10 ft)
Find the shear over panel CD
VCD= - x/50
At x=0, VCD = 0
At x=10, VCD = -0.2
Find moment at E = +(x/50)(10)=+x/5
At x=0, ME=0
At x=10, ME=+2.0
D
C
Shear is -ve
RF=x/50
F
F
RF=x/50
E
+ve moment

## Slide 28: Continuation of the Problem
-ve
0.2
2.0
+ve
x
I. L. for VCD
I. L. for ME

## Slide 29: Problem Continued - 5.5.3 Place load over region B´C´ (10 ft < x < 20ft)
VCD = -x/50 kip
At x = 10 ft
VCD = -0.2
At x = 20 ft
VCD = -0.4
ME = +(x/50)(10)
= +x/5 kip.ft
At x = 10 ft, ME = +2.0 kip.ft
At x = 20 ft, ME = +4.0 kip.ft
D
F
C
Shear is -ve
RF = x/50
D
F
RF = x/50
E
Moment is +ve

## Slide 30
0.4
0.2
-ve
x
B´
C´
I. L. for VCD
+ve
4.0
2.0
I. L. for ME

## Slide 31: 5.5.4 Place load over region C´D´ (20 ft < x < 30 ft)
When the load is at C’ (x = 20 ft)
C
D
RF=20/50
=0.4
Shear is -ve
VCD = -0.4 kip
When the load is at D´ (x = 30 ft)
A
RA= (50 - x)/50
B
C
D
Shear is +ve
VCD= + 20/50
= + 0.4 kip

## Slide 32
ME = + (x/50)(10) = + x/5
E
RF= x/50
+ve moment
-ve
A
B
C
D
A´
B´
C´
D´
x
+ve
0.4
0.2
I. L. for VCD
+ve
2.0
4.0
6.0
I. L. for ME
Load P

## Slide 33
5.5.5 Place load over region D´E´ (30 ft < x < 40 ft)
A
B
C
D
E
RA= (1-x/50)
Shear is +ve
VCD= + (1-x/50) kip
RF= x/50
Moment is +ve
E
ME= +(x/50)(10)
= + x/5 kip.ft
At x = 30 ft, ME = +6.0
At x = 40 ft, ME = +8.0

## Slide 34
A´
B´
C´
D´
E´
x
0.4
0.2
+ve
+ve
8.0
6.0
4.0
2.0
I. L. for VCD
I. L. for ME
Problem continued

## Slide 35
5.5.6 Place load over region E´F´ (40 ft < x < 50 ft)
VCD = + 1-x/50 At x = 40 ft, VCD= + 0.2
At x = 50 ft, VCD = 0.0
x
1.0
A
B
C
D
E
RA= 1-x/50
Shear is +ve
ME= + (1-x/50)(40) = (50-x)*40/50 = +(4/5)(50-x)
B
C
D
E
F
A
x
RA=1-x/50
At x = 40 ft, ME= + 8.0 kip.ft
At x = 50 ft, ME = 0.0
Moment is +ve

## Slide 36
A´
B´
C´
D´
E´
F´
x
1.0
0.2
0.4
0.4
0.2
2.0
4.0
6.0
8.0
I. L. for VCD
I. L. for ME
-ve
+ve
+ve

## Slide 37
5.6 INFLUENCE LINES FOR TRUSSES
Draw the influence lines for: (a) Force in Member GF; and
(b) Force in member FC of the truss shown below in Figure below
20 ft
20 ft
20 ft
F
B
C
D
G
A
E
600
20 ft
10(3)1/3

## Slide 38
Problem 3.7 continued -
5.6.1 Place unit load over AB
(i) To compute GF, cut section (1) - (1)
Taking moment about B to its right,
(RD)(40) - (FGF)(103) = 0
FGF = (x/60)(40)(1/ 103) = x/(15 3) (-ve)
At x = 0,
FGF = 0
At x = 20 ft
FGF = - 0.77
(1)
(1)
A
B
C
D
G
F
E
x
1-x/20
x/20
1
600
RA= 1- x/60
RD=x/60

## Slide 39
PROBLEM 5.6 CONTINUED -
(ii) To compute FFC, cut section (2) - (2)
Resolving vertically over the right hand section
FFC cos300 - RD = 0
FFC = RD/cos30 = (x/60)(2/3) = x/(30 3) (-ve)
reactions at nodes
x
1
1-x/20
x/20
(2)
(2)
300
600
A
B
C
D
G
F
E
RA =1-x/60
RD=x/60

## Slide 40
At x = 0, FFC = 0.0
At x = 20 ft, FFC = -0.385
I. L. for FGF
I. L. for FFC
0.77
20 ft
-ve
0.385
-ve

## Slide 41
PROBLEM 5.6 Continued -
5.6.2 Place unit load over BC (20 ft < x <40 ft)
[Section (1) - (1) is valid for 20 < x < 40 ft]
(i) To compute FGF use section (1) -(1)
Taking moment about B, to its left,
(RA)(20) - (FGF)(103) = 0
FGF = (20RA)/(103) = (1-x/60)(2 /3)
At x = 20 ft, FFG = 0.77 (-ve)
At x = 40 ft, FFG = 0.385 (-ve)
(1)
(1)
A
B
C
D
G
F
E
x
(40-x)/20
(x-20)/20
1
reactions at nodes
20 ft
RA=1-x/60
RD=x/60
(x-20)
(40-x)

## Slide 42
PROBLEM 5.6 Continued -
(ii) To compute FFC, use section (2) - (2)
Section (2) - (2) is valid for 20 < x < 40 ft
Resolving force vertically, over the right hand section,
FFC cos30 - (x/60) +(x-20)/20 = 0
FFC cos30 = x/60 - x/20 +1= (1-2x)/60 (-ve)
FFC = ((60 - 2x)/60)(2/3) -ve
x
1
(2)
300
600
A
B
C
D
G
F
E
RA =1-x/60
RD=x/60
(40-x)/20
(x-20)/20
(2)
FFC

## Slide 43
At x = 20 ft, FFC = (20/60)(2/ 3) = 0.385 (-ve)
At x = 40 ft, FFC = ((60-80)/60)(2/ 3) = 0.385 (+ve)
-ve
0.77
0.385
-ve
0.385
I. L. for FGF
I. L. for FFC

## Slide 44
PROBLEM 5.6 Continued -
5.6.3 Place unit load over CD (40 ft < x <60 ft)
(i) To compute FGF, use section (1) - (1)
Take moment about B, to its left,
(FFG)(103) - (RA)(20) = 0
FFG = (1-x/60)(20/103) = (1-x/60)(2/3) -ve
At x = 40 ft, FFG = 0.385 kip (-ve)
At x = 60 ft, FFG = 0.0
(1)
(1)
A
B
C
D
G
F
E
x
(60-x)/20
(x-40)/20
1
reactions at nodes
20 ft
RA=1-x/60
RD=x/60
(x-40)
(60-x)

## Slide 45
PROBLEM 5.6 Continued -
(ii) To compute FFG, use section (2) - (2)
Resolving forces vertically, to the left of C,
(RA) - FFC cos 30 = 0
FFC = RA/cos 30 = (1-x/10) (2/3) +ve
x
1
(2)
300
600
A
B
C
D
G
F
E
RA =1-x/60
(60-x)/20
(x-40)/20
FFC
RD=x/60
x-40
60-x
reactions at nodes

## Slide 46
At x = 40 ft, FFC = 0.385 (+ve)
At x = 60 ft, FFC = 0.0
-ve
0.770
0.385
-ve
+ve
I. L. for FGF
I. L. for FFC
0.385

## Slide 47
5.7 MAXIMUM SHEAR FORCE AND BENDING MOMENT
UNDER A SERIES OF CONCENTRATED LOADS
Taking moment about A,
RE  L = PR [L/2 -
a1
a2
a3
PR= resultant load
a1
a2
a3
PR= resultant load
C.L.
x
L/2
L
RE
A
B
C
D
E
P1
P2
P3
P4
P1
P2
P3
P4
RA

## Slide 48
Taking moment about E,
The centerline must divide the distance between the resultant of
all the loads in the moving series of loads and the load considered
under which maximum bending moment occurs.

## Slide 49
ABSOLUTE MAXIMUM SHEAR AND MOMENT
Maximum moment on the beam subjected to the moving load is located on the beam’s centreline between the resultant force and the nearest point.
Absolute maximum moment in simply supported beam occurs under one of the concentrated forces series.
This principle will have to be applied to each load in the series and the corresponding maximum moment is computed.
  By comparison, the largest moment is the absolute maximum.

## Slide 51
EXAMPLE :
Determine the absolute maximum moment in the simply supported beam

## Slide 56: Thank You